## Slide 1: Laboratory Mathematics and Measurements
Accurate values and measurements

## Slide 2: Importance of Mathematics in Laboratory
1. Reporting of time sample collected.
2. Amount of analyte in specimen
3. Volume of Specimen
4. Dilutions used in sample preparation and for recording QC.

## Slide 3: Time
Time of day critical in patient care
  Medication administered on schedule
  Diets and time of meals
  Specimens must be collected at correct time.
24 hour clock
  Avoid confusion with Greenwich clock which uses AM (mornings) PM (Afternoon)

## Slide 4: 24 Hour Clock
Military time
  Expressed in four digits (0000)
  Termed hundred hours. Noon = 1200 hours where midnight is 0000 or 2400.
  Based on 60 minute hour so that 5:35 pm = 1735

## Slide 5: Measuring Temperature
Two scales used for measuring temperature
  Each is divided into units = degrees°
Fahrenheit scale is English system therefore more common in US
Celsius scale Centigrade scale used in countries using metric system

## Slide 6: Temperature
Celsius
  Water freezes at 0° and boils at 100 °
Fahrenheit scale
  Water freezes at 32° and boils at 212°
Conversion Formula:
  °C = (F-32)x 5/9
  °F = (Cx9/5) + 32

## Slide 7: Common Laboratory Temperatures F C
Refrigerator temperature 35°- 46° 2°-8°
Freezer temperature 32° 0°
Room temperature 59° - 86° 15° - 30°
Incubator temperature 98.6° 37°
Body temperature 98.6° 37°
Autoclave temperature 254° 121°

## Slide 8: Units of Measurement
English System of measurement
  Ounces and pounds = weight
  Inches and feet = length
  Cups and quarts = volume
Metric System for Laboratory (SI) Systeme International.
  Important to memorize and practice these systems so one can communicate professionally

## Slide 9: Metric System
Based on decimal system
Basic units and prefixes that indicate a system of division in multiples of ten.
Basic units
  Weight = Grams
  Length = Meters
  Volume = Liter
Prefixes are added to each symbol to reduce or enlarge them by units of ten

## Slide 10: Metric System
Rules
  Use Arabic numerals with decimals to represent any fractions
    Example 1.25 rather than 1¼
  If quantity is less than 1, include a zero (0) before the decimal point. Delete any other zeros that are not necessary.
    Example: Do not write .750, instead write 0.75; adding a zero before the decimal point and deleting the unnecessary zero at the end.

## Slide 11: Metric System
Rules
  Write the unit after the quantity
    Write 30 mg not mg30 or 30mg
  Use lowercase letters for metric abbreviations. However use uppercase L to represent liter.
      Example: Write mg not MG. Write mL not ml. While ml is technically correct, you will avoid errors if you use an uppercase L.

## Slide 12: Let’s Practice
6 2/8 =
½ =
Two and one half kilograms
Four hundredth of a gram
31 millimeters
9 and one quarter milligrams

## Slide 13: Metric System
Basic unit of measure for weight is grams
Basic unit of measure for volume is liters
Basic unit of measure for length is meter
Cubic centimeter and milliliter are used interchangeably in clinical lab.
Quantitative test results are reported using the appropriate units of measurement.

## Slide 14: Common Units of Measurement
mg, U, g, dL. L
Other units of measure used mm, cm, mcg, mg, g, mcL, mL, L and cc
SI units is a system of reporting numbers that has been recognized by international organizations such as WHO.
Many countries have adopted its use, the United States has not completely converted to the SI system.

## Slide 15: SI System
Adaptation of the metric system that uses several of the basic units.
Some may be different for reporting results.
  Example: Blood glucose is reported in millimoles per liter (mmol/L) and hemoglobin is reported in grams per liter (g/L)
Important for MA double check the laboratory’s standard and include the appropriate units of measurement when reporting test values.

## Slide 16: Measuring Liquids
Vessels used to measure volume in the laboratory:
  Plastic and disposable for infection control purposes
  Beakers – used for estimating volumes
  Erlenmeyer flasks – used for reagent preparation and like beakers are not calibrated.

## Slide 17: Measuring Liquids
Graduated cylinders are used for measuring exact amounts of liquid.
The size of the cylinder should be matched as closely as possible to the volume of liquid being measured to obtain most accurate reading. Give examples.

## Slide 18: Volumetric Glassware

## Slide 19: Volumetric Glassware
Must go through rigorous calibration to ensure the accuracy of the measurement.
Pipettes are used extensively in the laboratory
  Used to deliver
  Used to transfer specific volumes of liquid
  Drawing liquid into the pipette requires a bulb or a vacuum pump-type device

## Slide 20: Pipettes
Two main types of manual pipettes are used
  Volumetric pipettes – used for transferring
  Graduated pipette – used for measuring
Graduated pipette
  Classified according to whether it contains or delivers the amount specified.
  A TD “To Deliver” delivers the specified volume by drawing the liquid up to the calibration mark and then allowing it to drain out vertically, unassisted.

## Slide 21: Pipettes
Volumetric continued:
  A small amount of liquid always remains in the tip of the pipette.
  A TC “To Contain” pipette must be emptied completely to deliver the specified amount.
  Serologic pipette – similar to a graduated pipette in appearance
    Tip is large permitting fast flow of liquid but less accuracy.
    This pipette is calibrated to the tip
    Should only be used for dilutions of serum and not for making reagents.

## Slide 22: Preparing Dilutions
Diluents used to dilute body fluids
  Water
  Saline solutions
  Buffer
Can be used for testing the strength of antibodies in serum.
Dilution refers to parts in total volume; it is a statement of relative concentration and represents expressions of concentration not expressions of volume.

## Slide 23: Dilutions
A one in ten dilution 1:10 can be prepared by measuring 1 mL of sample and diluting it with diluent to 10 mL.
9 mL of diluent is added
One can also be made with 2mL of sample.

## Slide 24: The End