## Slide 1: Laboratory Equipment

## Slide 2: Microscope
Indispensable instrument
Used to view objects too small to be seen with the naked eye.
Used:
  Evaluated stained blood smears
  Urine sediment
  Vaginal secretions
  Smears made from body fluids
  Microbiological cultures

## Slide 3: Microscope
Have three components
  Magnification system
  Illumination system
  Framework: includes all components responsible for positioning the slide and focusing.
Magnification System
  Ocular lens
  Objective lens

## Slide 4: Microscope

## Slide 5: Microscope
May be monocular or binocular (eyepiece)
  Monocular one eyepiece
  Binocular two eyepieces
  Located at top of the microscope
  Usual magnification of oculars is 10x
  Compound microscopes have objective lenses that increase the magnification of the specimen
  Objective lenses are attached to the revolving nosepiece
  Most microscopes have 4 different objective each with a different magnifying power.

## Slide 6: Microscope
Objective lenses
  Shortest objective has the lowest power (4x) Called a scanning lens.
  Next sized lens is 10x
  High dry 40-45 x
  Longest objective ( oil immersion) (100x)
    Uses special oil Immersion Oil The oil prevents refraction of the light and improves the resolution (clarity) of the magnified image.
    Oil immersion is used to view cells and extremely small materials such as bacteria and platelets and to examine stained specimens.
  To determine magnification of the specimen multiply the magnification of the objective lens by 10 (magnification of the ocular).

## Slide 7: Microscope
Arm of the microscope connects the objectives and the oculars to the base which supports the microscope and contains its light souce.
Stage of the microscope holds the slide to be viewed.
The light source, condenser, and the iris diaphragm make up the illumination system.
Condenser directs light up through the stage
The iris diaphragm regulates the amount of light passing through the specimen.

## Slide 8: Microscope
Above the base are the focusing knobs
  Coarse adjustment is used only with scanning and low-power lenses
  Fine adjustment is used with high power and oil immersion lenses.
Maintenance of microscope
  Dependent on the amount of daily use.
  Dirt is the primary enemy of the microscope
  Oil, makeup, dust and eye secretions all can obstruct vision through the lens and may also transmit infective organisms.
  Always store in a plastic dust cover when not in use.
  Lenses should be cleaned before and after each use with lens paper and cleaner. Solvent cleaner such as xylene is not recommended.

## Slide 9: Microscope
Should be placed in a permanent location
Moving a microscope:
  Carry securely with one hand supporting the base and the other holding the arm.
  When stored it should be left covered and with the low-power objective in the lowest position. Stage should be centered.
Using a microscope involves focusing and illumination
  Image is focused by moving the objective closer to the specimen
  illumination is accomplished by raising or lowering the condenser and by moving the specimen closer to or farther from the objective.

## Slide 10: Microscope
Focused through movement of the objective or stage controlled by knobs on both sides of the microscope.
Proper focusing begins with the objective at lowest power.
Course adjustment moves the objective very quickly.
Course knob is used first to bring the specimen into approximate focus.
Fine adjustment brings the specimen into precise focus. Fine focus moves the objective more slowly to allow the viewer to zero in on the specimen with greater accuracy.

## Slide 11: Centrifuge
Used when solids must be separated from liquids
Used increased gravitational force achieved by rapid spinning.
Separates:
  Blood cells from serum
  Cells and crystals from urine
  Used in many areas of clinical laboratory

## Slide 12: Centrifuge
Types
  Bench-top
  Floor models
  Some may be refrigerated.
  Some may have rotors or heads that are interchangeable.
Centrifuges
  Fixed angle rotors: specimen cups are held in a rigid position at a fixed angle
  Horizontal head with swinging buckets that swing out horizontally during centrifugation.
  A third type that is used for centrifuging capillary tubes for microhematocrit determination.
  Centrifuges also may be equipped with timers to automatically stop at set time.

## Slide 13: Centrifuge
Using a centrifuge usually are given in terms of revolutions per minute RPM
Spinning generates centrifugal force
General laboratory centrifuges operate at up to 6,000 rpms generating a relative centrifugal force of up to 7,300 times the force of gravity.
Conventional horizontal centrifuges attain speeds of up to 3,000 rpm angle-head centrifuges can attain higher speeds (up to 7,000 rpm)

## Slide 14: Centrifuge
Mechanical hazard
  Centrifuges can be dangerous if not used correctly.
  Ensure that the centrifuge is balanced so that tubes of equal size and containing equal volume are directly across from on another in the rotor holders.
  Always an even number of tubes in the centrifuge. If a second specimen of the same volume in the same-size tube is not available for balance, a tube of water may be used to balance the load.
  Tube should be capped to prevent emission of aerosols.
  Rubber cups should be placed in the bottom of the carrier cups to prevent breakage of glass tubes.

## Slide 15: Centrifuge
Mechanical hazards
  Never be opened while in operation
  Never slow a centrifuge with hands
  Use brake if equipped only in an emergency. Most common emergency is broken glass tube. Wait until centrifuges comes to a complete stop and follow the manufacturer’s instructions for disinfecting the unit.
  Follow Standard Precautions to prevent injury and disease transmission.
Maintenance
  Check, clean and lubricate regularly to ensure proper operation.
  Certified technician must use a photoelectric device or a strobe tachometer to ensure the centrifuges speed to comply with QA guidelines.

## Slide 16: Incubator
Cabinets that maintain constant temperatures
Generally used in microbiology and sometimes in chemistry
Hold constant temperature of 95°F to 98.6°F ( 35°-37°C). Other temperatures may also be used.
Some are enriched with Carbon Dioxide gas (CO2) to enhance the growth of pathogenic bacteria.
A pressurized tank of CO2 is attached to the cabinet and the concentration is maintained at 10%.
Incubators may have warning alarms that sound if the temperature exceeds or falls below a specified range

## Slide 18: Incubator

## Slide 19: Incubator
Maintenance
  Temperature should be checked daily
  Cabinets should be cleaned regularly with disinfectant approved by the manufacturer.

## Slide 20: Autoclave

## Slide 21: Autoclave
Strict QA methods must be followed when an autoclave is used.
A certified technician should regularly examine the autoclave and biologic and chemical indicators should be checked daily.
Biologic indicators include spore preparations that are wrapped in the autoclave load.
At the end of the sterilization period, they are incubated and checked for germination.
If the spores fail to germinate the autoclave reached the appropriate temperature.

## Slide 22: The End