## Slide 1: Routine Urinalysis

## Slide 2: Routine Urinalysis
Patient Preparation
  Request may be embarrassing for patient…….be sensitive
  Make request in private in exam room
  Give explicit instructions for patient to understand process and what to expect.
  MA should use therapeutic communication to explain the details of the procedure to the patient and be observant of confusion.
    Language barriers if they exist

## Slide 3: Routine Urinalysis
Container
  Important for collection container to be scrupulously clean
  Laboratory should provide specimen container
    Patient should not use jars from home
    Disposable, nonsterile, plastic or coated paper containers are the most common and are available in many sizes with tight fitting lids
    For C&S container must be sterile; and patient must be instructed on how to collect the specimen and how to handle the sterile specimen cup.
      Pliable polyethylene bags with adhesive are used to collect urine from infants and children who are not toilet trained.
    For timed or 24 hour specimens a large, wide mouth plastic container with screw-cap tops are used.
    Most routine UA testing, pregnancy testing and tests for abnormal analytes are performed on urine collected in non sterile containers.

## Slide 4: Routine Urinalysis
Containers
24 hour urine container
Pediatric collection
Sterile collection for C&S
Non sterile container

## Slide 5: Routine Urinalysis
Methods of Specimen Collection:
  Random specimen: freshly voided urine collected in clean containers.
  First morning specimen: Collected when the patient arises in the morning.
    Most concentrated and best for nitrite and protein determination, bacterial culture, pregnancy testing and microscopic examination.
  2 Hour post-prandial urine specimens: Collected 2 hours after a meal
    Used for diabetes screening and for home diabetes testing programs.
  24 hour urine specimen – collected over a 24 hour period
    Useful for quantitative chemical analysis such as hormone levels and creatinine clearance rates (evaluation of glomerular filtration rate of the kidneys)

## Slide 6: Routine Urinalysis
Methods of collection:
  Clean catch mid-stream specimen (CCMS) useful for UA and C&S
  Catheterized specimens – Physician, PA, Nurse must insert a sterile catheter into bladder to collect specimen.
  Suprapubic specimen: collected with needle inserted directly into the bladder.
Specimen
  Minimum volume = 12mL but 50mL is preferred.
  Imperative patient receive adequate verbal and / or written instructions.
  Rule of thumb or easiest directions for the patient are to ask the person to “Fill the container halfway”.

## Slide 7: Routine Urinalysis
Handling and Transport of Specimens
  Chemical and cellular components of urine change if the urine is allowed to stand at room temperature (RT).
  Specimens refrigerated and processed within 1 hour of collection.
    NOTE: Specimen must come to RT when testing with chemistry strips as some of the elements are temperature dependent.
  Transported specimens to a referral lab – specimens transported in evacuated transport tubes which contains preservatives and look similar to blood collection tubes. 7-8 mL of urine can be collected into the tubes.

## Slide 8: Routine Urinalysis
Changes in Urine at RT
  Clarity Becomes cloudy as crystals precipitate and bacteria multiply
  Color May change if pH becomes alkaline
  pH Becomes alkaline as bacteria form ammonia from urea
  Ketones Decrease because of evaporation
  Bilirubin /urobilinogen
  Blood May hemolyze; false positive results are possible because of bacterial peroxidase
  Nitrite May become positive as bacteria multiply and reduce nitrate.
  Casts Lyse or dissolve in alkaline urine
  Cells Lyse or dissolve in alkaline urine

## Slide 9: Routine Urinalysis
Bacteria Multiply twofold approximately every 20 minutes
Yeasts Multiply
Crystals Precipitate as urine cools; may dissolve if pH changes.

## Slide 10: Routine Urinalysis
Physical Examination of Urine
  Appearance
    Color – Shade of yellow, ranging from pale straw to yellow to amber.
    Depends on the concentration of pigment Urochrome and amount of water in specimen.
    Variations in color may be caused by diet, medication and disease.
    Abnormal colors may be related to pathologic or nonpathologic factors.
  Color
    Abnormal Urine colors
      Yellow – brown – caused by bilirubin resulting from excessive RBC destruction or bile duct obstruction.
      Orange –yellow – caused by bilirubin or urobilinogen resulting from a reduction in the functioning of liver cells or excessive RBC destruction.
      Green – caused by biliverdin resulting from oxidation of bilirubin.

## Slide 11: Routine Urinalysis
Abnormal Color
  Dark red- caused by erythrocytes resulting from bleeding of urinary structures, menstrual cycle, or hemoglobin from the breakdown of erythrocytes.
  Red-brown – caused by erythrocytes and hemoglobin or myoglobin (skeletal or cardiac muscle breakdown)
  Clear red - caused by hemoglobin and porphyrin products.
  Cloudy red – caused by intact erythrocytes

## Slide 12: Routine Urinalysis

## Slide 13: Routine Urinalysis
Odor
  Fresh urine specimen usually has a slightly aromatic odor. Odor is not usually recorded in a urinalysis, but some characteristic odors may indicate certain conditions.
    Ammonia odor: may indicate bacteria in the urine. Also if urine has been left standing at RT, the urea converts to ammonia.
    Sweet or fruity odor: may be an indication of the presence of ketones. Ketones are an intermediate product of fat metabolism found in patients with uncontrolled diabetes and patients on low-carbohydrate diets.
    Foul odor: Characteristic of a Urinary Tract Infection (UTI). The longer the urine stands the worse the odor becomes. Decomposition of WBCs (leukocytes) causes the foul odor.

## Slide 14: Routine Urinalysis
Odor
  Musty odor: can be caused by certain foods, such as asparagus, or by an inherited metabolic condition phenylketonuria (PKU) that occurs in newborns. If PKU is left untreated it may lead to mental retardation of child.
Foam:
  Normally the presence of foam is not recorded, however careful observation of this property can be significant clue to an abnormality.
    White foam: can indicate presence of increased protein.
    Greenish yellow foam: means Bilirubinuria which can be due to hepatitis.

## Slide 15: Routine Urinalysis
Appearance / Turbidity/ Clarity
  Done the same time the color is evaluated.
  Requires a clear container for accuracy.
  Terms used to describe appearance:
    Clear
    Hazy (slightly cloudy)
    Cloudy
    Turbid (very cloudy)
  Substances that may cause a freshly voided urine to appear cloudy are bacteria, yeast, blood cells, casts, mucous threads, and sperm.
  These substances could be clinically important and are evaluated further in the chemical and microscopic parts of the UA.

## Slide 16: Routine Urinalysis
Specific Gravity
  Weight of a substance compared with the weight of an equal volume of distilled water.
  The Specific Gravity of distilled water is 1.000
  The normal specific gravity of urine ranges from 1.005 – 1.030 depending on patient fluid intake. Most fall between 1.010 – 1.025
  Urine specific gravity indicates whether the kidneys are able to concentrate the urine and is one of the first indications of kidney disease.
  Presence of glucose, protein, or an x-ray contrast medium used in diagnostic studies also may increase the specific gravity of urine.

## Slide 17: Routine Urinalysis
Measure of Specific Gravity; laboratories may use:
  Urinometer
  Refractometer
  Chemical reagent strip
Urinometer
Refractometer
Chemistry Strips

## Slide 18: Routine Urinalysis
Urinometer
  Sealed glass float with calibrated paper scale in it’s stem.
  Slight spinning motion, Urinometer is placed in a cylinder containing a urine sample and value is read.
  Must have 20 - 25mL; if not enough urine for test report out results as QNS
  Considered the “Gold Standard” of specific gravity testing.
Refractometer measures the refraction of light through solids in a liquid. The result is called the “Refractive Index”.
  Faster and easier to use than Urinometer and requires only one drop of urine.
  Refractometer must be calibrated daily with distilled water, which should read 1.000.

## Slide 19: Routine Urinalysis
Reagent strip (dipstick) test is the method most commonly used in POL.
It is a waived test.
The pad on the strip contains a chemical that is sensitive to positively charged ions, such as sodium (Na) and potassium (K).
Detects specific gravity in the range of 1.005 – 1.030.

## Slide 20: Routine Urinalysis
Chemical Urinalysis
  Second part of UA is chemical testing
  Helps in the diagnosis of pathological conditions
  Reagent Strips
    Thin plastic strip containing pads impregnated with chemical reagents that test for specific substances.
    When each reagent pad reacts with its specific analyte a color change occurs.
    The more of a particular analyte that is present in urine the darker the color will be on the reagent pad.

## Slide 21: Routine Urinalysis
Reagent strips
  Semiquantitative testing: Testing determines the approximate quantity of an analyte.
  Qualitative testing: Indicates whether an analyte is present.
  Quantitative testing: Measures the exact amount of a substance and usually requires more complex equipment and procedures not usually available in a POL.
  They are time dependent; each test must be read at a specific time.
  Tests on strip are referred to as “Screening tests” if results are abnormal then additional testing may be performed.

## Slide 22: Routine Urinalysis
Chemical Strips Quality Assurance
Guidelines to follow:
  Reagent strip bottle must be kept tightly closed when not in use because moisture from air light and aerosols can affect the accuracy of the testing.
  Pads on strip should not be touched or placed on any surface.
  Keep the reagent strips in a cool dry place but do not refrigerate them.
  Do not use an expired bottle.
  Any bottle that has been open longer than 2 months should not be used because of repeated exposure to air, moisture etc.

## Slide 23: Routine Urinalysis
Guidelines to follow:
  Do not combine strips from different bottles.
  Follow all manufacturers directions.
  Mix urine specimen well and bring to room temperature.
  Make sure all pads are covered with the specimen.
  Do not leave the strips in the urine too long because the chemicals in the pads can “leach” (wash out) into the urine
  When taking the strip out of the urine remove excess urine by pulling the back side of the strip against the container and then briefly blot the side of the strip against absorbent paper.

## Slide 24: Routine Urinalysis
Guidelines to follow:
  Hold the strip horizontally to keep the colors on one pad from running into another while you are comparing the colors to the reference testing chart. Do not touch the bottle with the strip while comparing .
  Record observed results for each analyte on lab log and requisition.
  Use Quality Control Strips to ensure accuracy of results.
Automation: Clinitek Analyzer
  Runs the chemical analysis according to the principle of “Reflectance Photometry”
  Micropressor controls the movement of the strip into the reflectometer where a light of specific wavelength is beamed into the strip.

## Slide 25: Routine Urinalysis
Clinitek
  Light that is reflected is measured and is converted into a digital reading and is printed.
  Timing and color interpretation are consistent and do not vary by machine as with individual readers.
  Disadvantage: With urines that contain a large amount of pigment, the machine cannot recognize this and this can result in false positives.

## Slide 26: Routine Urinalysis
Specific Gravity
  Normal range 1.005 – 1.030
  Indicates kidney ability to concentrate urine
  Pathological conditions that increases urine concentration are:
    Adrenal insufficiency
    Congestive heart failure
    Hepatic disease
    Glycosuria (sugars in the urine)
    Dehydration caused by fever, vomiting and diarrhea.

## Slide 27: Routine Urinalysis
Specific Gravity
  Pathological conditions that decreases urine concentration are:
    Chronic renal insufficiency
    Diabetes insipidus
    Malignant hypertension
  The first morning urine is more concentrated and therefore a higher specific gravity.
  Urine becomes more dilute as fluids are consumed throughout the day.

## Slide 28: Routine Urinalysis
pH
  Measures the level of acidity or alkalinity.
  Lungs and kidneys function to maintain the body’s acid alkaline balance.
  A pH of 7.0 is neutral. 0-6 is acid and 8-14 is alkaline. Blood pH should range between 7.35 -7.45. Below 7.35 – the body is in acidosis; above 7.45 – the body is in alkalosis.
  Normal urine pH 5-8 with the average being 6.0 slightly acid. Urine pH must be measured on a freshly voided specimen because bacteria converts urea to ammonia in urine that has been sitting at room temperature. This conversion causes the urine to become alkaline and indicate a UTI

## Slide 29: Routine Urinalysis
pH

## Slide 30: Routine Urinalysis
Glucose
  Not normally found in urine.
  Glucose is filtered into the glomerular filtrate and in renal tubule this substance is reabsorbed into the blood. However if the level in the blood has surpassed the renal threshold then it cannot be reabsorbed.
  Renal threshold 160 – 180 mg/dL
  Glucose in urine = glycosuria
  Other sugars in urine: lactose, fructose, galactose and pentose.
  Test strip uses enzymatic reaction using the enzyme glucose oxidase.
  Glucose in urine as a result of diabetes mellitus; also after vigorous exercise or acute emotional stress.

## Slide 31: Routine Urinalysis
Glucose:
  False positive glucose test
    Large quantities of aspirin
    Ascorbic acid (vitamin C)
    Medications containing Levadopa
  Clinitest is a confirmatory test to determine if other sugars or reducing substances (substances that easily lose electrons) in addition to Glucose are present.
  Galactosemia rare metabolic condition in which the body is not able to convert galactose to glucose resulting in excretion of galactose in the urine.

## Slide 32: Routine Urinalysis
Galactosemia
  In infants results in failure to thrive
    Anorexia
    Vomiting and diarrhea
    Enlargement of liver and spleen
    Cirrhosis
    Cataracts and mental retardation
    Extreme cases can result in permanent brain damage and death.
    A positive clinitest and a negative test strip for glucose can indicate galactose in the urine.
  Lactose may be found in the urine of pregnant women and in rare cases fructose and pentose can be found in urine because of high consumption of honey or fruit.

## Slide 33: Routine Urinalysis
Ketones:
  Product of fat metabolism that are then oxidized by the muscles.
  Excessive fat metabolism leads to large amounts of ketones that the muscles cannot oxidized. Large amounts of ketones in blood subsequently is found in the urine: This is known as ketonuria.
  Ketones and glucose in urine = uncontrolled diabetes mellitus.
  Ketones are acid compounds therefore ketonuria is correlated with a low pH.
  If Glucose, Ketones and acidity are all present in urine this may indicate a condition known as ketoacidosis. This can lead to diabetic coma.

## Slide 34: Routine Urinalysis
Ketones:
  Other conditions causing ketonuria
    Fever
    Starvation
    Anorexia
    Prolonged vomiting
    Diets high in fat and low in carbohydrates.
  Ketones evaporate at RT; therefore urine must be tested immediately or tightly capped and refrigerated.
  Confirmatory test for positive test strip is the Acetest.

## Slide 35: Routine Urinalysis
Bilirubin
  RBC (lives 120 days) …..cell dies and releases hemoglobin.
  Heme, a product of hemoglobin decomposition, subsequently breaks down to form bilirubin. Bilirubin at this point attaches to a protein (albumin) in the blood and is not water soluble and cannot because of its size does pass through the glomerulus. Once the protein bound bilirubin passes through the liver it becomes water soluble. It then enters the gall bladder and is excreted into the intestines. In the intestine it is known as urobilinogen.
  Bilirubin therefore is normally not found in the urine.

## Slide 36: Routine Urinalysis
Bilirubin
  Elevated levels in urine as a result of:
    Hepatitis
    Excessive hemolysis of RBCs
    Liver damage
    Obstruction of the bile ducts.
  Color of urine with excessive Bilirubin can be yellow orange to yellow brown
  Yellow foam when shaken
  A positive test strip for bilirubin can be confirmed with a specific test known for bilirubin Ictotest.

## Slide 37: Routine Urinalysis
Urobilinogen:
  Small amounts may be present in the urine. It is mainly excreted by the intestines in the feces.
  Urobilinogen may be increased:
    Excessive hemolysis of RBCs
    Cirrhosis
    Infectious mononucleosis
    Congestive heart failure.

## Slide 38: Routine Urinalysis
Blood
  Three types of blood components give positive reagent strip reaction for blood.
    Intact RBCs = Hematuria; usually occurs with UTI associated with bleeding, such as cystitis and urethritis. Kidney stones, tumors and lesions may also cause bleeding.
    Hemoglobin = hemoglobinuria; caused by transfusion reactions, malaria, drug reactions, snake bites and severe burns. Because it is the result of hemolyzed RBCs that are no longer visible it is termed “Occult Blood”.
    Myoglobin = an oxygen storing pigment of muscle tissue, can be found in urine after massive muscle injury, physical trauma or electrical injury.

## Slide 39: Routine Urinalysis
Protein
  One of the first signs of renal disease is proteinuria….large amounts of protein in the urine.
  Normally proteins are too large to pass through the glomerulus.
  Small amounts of protein may be present in urine and not be pathogenic for example:
    Fever
    Exposure to heat or cold
    Excessive exercise
    Emotional stress

## Slide 40: Routine Urinalysis
Protein found in urine
  Albumin - Strenuous physical exercise; emotional stress; pregnancy; Infection, Glomerulonephritis; neonates first week.
  Globulins – Glomerulonephritis; renal tubular dysfunction
  Hemoglobin – Hematuria; Hemoglobinuria
  Nucleoprotein – White blood cells in urine; Epithelial cells in urine.
  Bence Jones – multiple myeloma; leukemia
  In addition pregnant women are routinely checked for protein in the urine because it may be a sign of preeclampsia.
Correlating protein with Specific Gravity is important because urine with a low Specific Gravity showing a trace or small amount of protein may be significant.

## Slide 41: Routine Urinalysis
Nitrites
  Nitrates are converted to nitrites by some bacteria
  First morning specimen needed for this test because urine is held in bladder for 4-5 hours giving bacteria time to convert nitrates to nitrites.
  Urine should not be left standing because bacterial contaminants can convert the nitrates to nitrites resulting in a false positive reaction.
  A positive nitrite test is usually correlated with a positive leukocyte test.

## Slide 42: Routine Urinalysis
Leukocytes:
  Determines the presence of leukocytes (WBC).
  Strip tests for esterase which is produced by lysed granulocytic WBC.
  Presence of WBCs usually indicates a URI and should be correlated with a nitrite test.

## Slide 43: The End